## Slide 1
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
FACE-LIGHT
국가암호공모전

## Slide 2
CONTENTS
01 02 03 04
Introduction
- AES
- Side Channel Attack
- Masking
- Outline
- Structure
- FACE-LIGHT
- Extended-FACE
- Evaluation
- Contribution
- Future Work
FACE
Our Work
Conclusion
국가암호공모전

## Slide 3
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
01
Introduction
FACE-LIGHT

## Slide 4: AES (Advanced Encryption Standard)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
01
Introduction
전세계 블록 암호 표준
  FIPS 197
  ISO/IEC 18033-3
다양한 모드 존재
  ECB, CBC, CFB, OFB, CTR
Fig 1. AES Structure

## Slide 5: AES-CTR
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
01
Introduction
AES Counter Mode
병렬처리 가능
128bits IV(Initial Vector)
  96bits Nonce
  32bits Counter
Counter만 1씩 증가
Fig 2. AES-CTR Structure

## Slide 6: Side Channel Attack(SCA)
연산 중 발생하는 부가적 요소를 이용한 공격
Power Analysis
  SPA(Simple Power Analysis)
  DPA(Differential Power Analysis)
  CPA(Correlation Power Analysis)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
01
Introduction
Fig 3. Power Analysis Attack

## Slide 7: Masking
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
01
Introduction
SCA Countermeasure
  전력 분석 방해
공개된[1] 마스킹 기법 응용
  8bits Microcontroller 최적 구현
Fig 4. Masking Process

## Slide 8
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
02
FACE
FACE-LIGHT

## Slide 9: Outline
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
02
FACE
AES-CTR의 특징을 활용한 최적화 구현 기법
  마지막 byte는 Counter 값을 저장
  첫 블록과 다음 블록의 차이는 마지막 byte
Counter를 제외하고 반복되는 부분을 저장
  사전 테이블(Look Up Table, LUT)로 저장
  특정 Round마다 정해진 LUT를 참조
  총 5개의 LUT가 필요 (약 5)
Counter 값 변화에 따라 일정 주기마다 LUT 업데이트 필요

## Slide 10
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
02
FACE

## Slide 11: Structure (Round 0)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
02
FACE
전체 데이터 중 마지막 byte의 변경을 활용
  첫 블록과 다음 블록의 차이는 마지막 1byte
Round 0 이후 12bytes 사용 가능
  S[12], S[13], S[14], S[15]
(232 – 1)번 만큼 테이블 사용 가능
  갱신이 필요 없음

## Slide 12: Structure (Round 1)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
02
FACE
마지막 byte의 확산
  두 단계에 걸쳐 확산
  ShiftRows
  MixColumns
LUT 생성 가능
  첫 열 제외
(28 – 1)번 만큼 테이블 사용 가능

## Slide 13: Structure (Round 1+)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
02
FACE
마지막 byte의 확산
  두 단계에 걸쳐 확산
  ShiftRows
  MixColumns
LUT 생성 가능
  S[15]를 index로 사용
  Table Size: 1
(28 x 232)번 만큼 테이블 사용 가능

## Slide 14: Structure (Round 2)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
02
FACE
첫 열 bytes의 확산
  두 단계에 걸쳐 확산
  ShiftRows
  MixColumns
Round 2 이후 모든 값 영향
LUT 생성 가능
  MixColumns의 중간 연산 값
(28 - 1)번 만큼 테이블 사용 가능

## Slide 15: Structure (Round 2+)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
02
FACE
Round 2의 LUT에 저장되지 않은 값
  S[0], S[1], S[2], S[3]
LUT 생성 가능
  미사용 값의 중간 값
  Table Size: 4
(28 x 232)번 만큼 테이블 사용 가능

## Slide 16
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
02
FACE
Limitation of FACE
8bits Microcontroller에서 사용하기 어려움
  LUT의 용량 문제
  최소 의 메모리 필요
일정 주기마다 LUT의 갱신이 필요
Fig 6. Arduino Uno Memory Structure

## Slide 17
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work
FACE - LIGHT
FACE-LIGHT

## Slide 18: Target Board
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work
8bits Microcontroller
  Arduino Uno ATmega328P
Hardware Spec
  Flash Memory: 32
  SRAM: 2
  EEPROM: 1
  Clock Speed: 16MHz
Fig 7. Arduino Uno

## Slide 19: Overview
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work
FACE에 기반한 최적화 구현 기법
  저전력 프로세스에 최적화 된 구현 기법
Counter값에 의존하는 반복 부분을 저장
  사전 테이블(Look Up Table, LUT)로 저장
  한번의 참조로 다수의 Round를 생략 가능
  총 4개의 LUT가 필요 (4)
Counter 값 변화에 따라 LUT 업데이트 필요 없음
기존 FACE와 결합하여 성능 향상

## Slide 20
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work
Fig 8. Overview of FACE-LIGHT

## Slide 21
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work

## Slide 22
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work

## Slide 23
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work

## Slide 24
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work

## Slide 25
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work

## Slide 26
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work

## Slide 27
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work

## Slide 28
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work

## Slide 29: Look Up Table Structure
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work
Fig 9. FACE-LIGHT Look Up Table
Size of LUT: 4
업데이트 필요 없음

## Slide 30: Extended FACE
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work
Extended FACE
  Original FACE
  FACE-Light
연산 절감 효과
  Subbytes
  AddRoundKey

## Slide 31: Evaluation (Calculating Speed)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work
Security Level | Dinu et al. [2] | Otte et al. [3] | FACE-Light (Our Work) | Ex-FACE (Our Work)
AES-128 | 2,835 | 2,507 | 2,218 | 1,967
AES-192 | N/A | 2,991 | 2,702 | 2,449
AES-256 | N/A | 3,473 | 3,184 | 2,931
Unit: Clock Cycles
표준 AES보다 약 22% 성능 향상을 보임
추가적인 LUT 업데이트 시간 소요가 없음
Table 1. Comparison of calculating speed

## Slide 32: Evaluation (vs FACE)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work
 | FACE | FACE-LIGHT (Our Work)
Table Update | O | X
Constant Timing | Not Support | Support
Target Processor | 32-bits or above | 8-bits or above
Expandable Round | Round 2 | Round 3
FACE-LIGHT 8bits Microcontroller에 최적화 됨
LUT 업데이트가 없기 때문에 Constant Timing 유지
8bits 저전력 프로세서부터 제약없이 사용 가능
Table 2. Comparison with original FACE

## Slide 33: Evaluation (Side Channel Attack Resistance)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work
파형 분석 공격(CPA, DPA)에 대한 저항성을 지님
Fig 10. Graph of Power Analysis

## Slide 34: Evaluation (vs LEA)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
03
Our Work
ARX 연산을 사용하는 LEA에 비해 매우 빠른 마스킹 속도
기존의 Masked AES 연구 결과에 비해 성능 향상
  FACE-LIGHT, 소프트웨어 최적화
LEA-128 [4] | Masked LEA-128 [5] | Masked AES-128 (Previous Work) [6] | Masked FACE-128 (Our Work)
2,688 | 36,589 | 25,970 | 6,219
Unit: Clock Cycles
Table 3. Comparison with LEA and Previous Work

## Slide 35
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
04
Conclusion
FACE-LIGHT

## Slide 36: Contribution
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
04
Conclusion
저전력 프로세스 상에서 AES-CTR의 효과적인 최적화
  Clock Cycles 최적화
FACE에 비해 더 많은 Round 확장 가능
Constant Timing을 통한 공격 지점 예측의 어려움
전력 분석 대응을 위한 Masking 적용
AES의 경량화

## Slide 37: Future Work
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
04
Conclusion
다양한 플랫폼 상에서의 최적화
  16bits MSP … ETC
다양한 국산 암호 제안 기법 적용
  사전 테이블 연산
  부채널 분석 내성
  소프트웨어 최적화
국제 저널 투고 시 SIMON/SPECK 등의 경량 암호와 비교
Fig 11. MSP430FR2433 LaunchPad kit

## Slide 38
THANK
YOU

## Slide 39: Code (Header)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
Appendix

## Slide 40: Code (Macro)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
Appendix

## Slide 41: Code (Main)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
Appendix

## Slide 42: Code (Table)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
Appendix

## Slide 43: Code (Masking)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
Appendix

## Slide 44: Code (Masking)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
Appendix

## Slide 45: Code (Keyschedule)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
Appendix

## Slide 46: Code (Keyschedule)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
Appendix

## Slide 47: Code (Encryption)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
Appendix

## Slide 48: Code (Encryption)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
Appendix

## Slide 49: Code (Encryption)
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
Appendix

## Slide 50
FACE–LIGHT: Fast AES CTR Mode Encryption for Low-end Microcontrollers
-
References
[1] C. Herbst, E. Oswald, and S. Mangard, “An aes smart card implementation resistant to power analysis attacks,” in International conference on applied cryptography and network security, pp. 239–252, Springer, 2006.
[2] D. Dinu, A. Biryukov, J. Großsch ̈adl, D. Khovratovich, Y. Le Corre, and L. Perrin,“FELICS–fair evaluation of lightweight cryptographic systems,” inNIST Workshopon Lightweight Cryptography, vol. 128, 2015.
[3] D. Otteet al., “AVR-crypto-lib,”Online: http://www. das–labor. org/wiki/AVR–Crypto–Lib/en, 2009.
[4] H. Seo, I. Jeong, J. Lee, and W. Kim, “Compact implementations of ARX-based block ciphers on IoT processors,” ACM TECS, 2018.
[5] E. Park, S. Oh, and J. Ha, “Masking-based block cipher LEA resistant to side channel attacks,” KIISC, 2017.
[6] K. H. Kim, H. J. Seo, “Implementation of Optimized 1st-Order Masking AES Algorithm Against Side-Channel-analysis,” KIPS, 2019.